## Slide 1: Ridership Forecasting with STOPS for Transit Project Planning
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 2: Content sourced from:
NTI/FTA STOPS Training Phoenix, June 2019
and
STOPS User Guide v2.50 DRAFT 2019-04-18

## Slide 3: Background
Simplified Trips-On-Project Software (STOPS)
  User Benefits  Trips On Project
  Originally intended for smaller regional agencies
Ridership Forecasting for project planning
  Not substitute for non-transit projects or RTP development
  Modelers should derive forecast insights from model outputs
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 4: STOPS and the FTA CIG Program
Discretionary Capital Investment Grants (CIG) Program
  FTA: project ratings and funding recommendations
  Several rating criteria dependent upon predicted riders
  STOPS origins in CIG streamlining (2009)
  STOPS provision of all CIG-required rider measures
  Evolution of STOPS capabilities
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 5: Topics
Design standards
National calibration
How STOPS works – Overview
OMPO STOPS
  Inputs – Networks and Other Data
  Schedule-Based Transit Path-Builder
  Current Year Travel Patterns
  Initial Travel Patterns for STOPS-Incremental
Mode & Path Choice
Calibration & Test Run
STOPS File Structure
STOPS Interface
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 6: Design Standards
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 7: Design Standards
FTA’s design standards for “a simplified method”
  Focus on trips on major-capital projects  STOPs
  Keep it simplified for users
  Make it reasonably accurate
  Make it operate on Windows-based computer
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 8: Design Standards and Outcomes
Outcomes in STOPS
  Fixed-guideway focus, but detailed system-wide representation
  Calibration against a range of rider-survey datasets
  Validation against a wide range of projects/systems
  Required inputs limited to readily-available sources
  Level of engagement at user option: simple to sophisticated
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 9: Design Standards and Outcomes
Outcomes in STOPS
  Efficient application on standard Windows computer
  GIS package is a necessary tool for some tasks
  No other transportation software needed, although scheduling software might be preferred to STOPS GTFS editor for transit networks
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 10: Model Application
Multiple application modes
  STOPS-synthetic
  STOPS-synthetic plus special markets
  STOPS-incremental
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC
Notes: Red arrow – STOPS Incremental for OMPO as 2012 Survey was available

## Slide 11: STOPS Application Modes
STOPS-synthetic
  Invents transit demand patterns from the CTPP worker flows, manipulated to match transit counts
Strength
Responds to mandate for simplified method to predict total number of trips on a project without lots of local data collection and model development/refinement
Weakness
May not predict the details of transit demand patterns sufficiently well to support other project-planning tasks
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 12: STOPS Application Modes
STOPS-synthetic plus special markets
  Adds data for important transit markets that are not related to worker flows and therefore cannot be predicted by STOPS-synthetic alone
Strength
Fills gaps in the representation of transit markets produced by STOPS-synthetic while minimizing data collection costs
Weakness
Adds costs and requires clear targeting of data collection from somewhat ambiguously defined “special” markets
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 13: STOPS Application Modes
STOPS-incremental (OMPO APPLICATION)
  Uses rider survey data (!) to represent current transit travel patterns thereby tasking the models only to predict changes in those patterns caused by transit service changes and growth
Strength
Forecasts are grounded in actual transit travel patterns rather than synthesized (made-up) model predictions of those patterns
Weakness
Time and cost of data collection; and applicability only to established transit markets
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 14: Choice of Application Mode
Depends, in part, on what you are doing:
  Just filling in FTA’s templates
  Just looking for a second number to compare with number prepared with local travel models
  Attempting to understand the ridership potential of a project under development
  Comparing ridership potential across alternatives
  Looking for details to help size facilities and refine the transit service plan
Less Rigor
More Rigor
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 15: Choice of Application Mode
Less rigor
  STOPS-synthetic “out of the box”
  Required inputs only; no counts; little calibration
  Just coding of the Build scenario
Increasing rigor
  Counts; additional data; closer calibration
  STOPS-incremental
  Probably more time, effort, and cost
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 16: Choosing an Application Mode
With a good rider survey already in hand and a project that serves a well-developed transit market
  Incremental approach calibrates more readily and has lower likelihood of travel-market distortions
  Therefore, STOPS-incremental is more likely to provide reliable predictions of future ridership patterns
  For larger, more complex, and riskier projects, the advantages of STOPS-incremental may suggest that the collection of rider survey data is desirable where appropriate data are not currently available
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 17: National Calibration
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 18: National Parameter Development
Traditional approach
  “Estimation” with econometric software
  Data from an individual metro area
  Struggles with relative values of parameters on highly inter-correlated attributes of travel modes and traveler characteristics
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 19: National Parameter Development
Approach for STOPS
  Starting-point parameter values
    Built on outcomes of 40 years of parameter estimation
    Constrained to be consistent in path-building and mode choice
  Iterative adjustment of starting-point parameters
    Adjustments made to path-building parameters to match paths reported in the surveys and by on-line path-finders
    Mode choice parameters revised accordingly
  Calibration and validation against datasets assembled from many metro areas and transit systems
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 20: National Parameter Development
STOPS comes with a “national” static calibration that tunes its default understanding of fixed-guideway trips and all transit trips by:
  Trip purpose, auto-ownership, and access mode
  Transit access/egress time, run-times, frequencies
  Fixed-guideway effects compared to local bus
Data are from database of published rider surveys, count data, and other ridership information
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 21: National Parameter Development
STOPS comes with a “national” dynamic validation that strengthens its ability to predict the ridership on new fixed-guideway projects
Data are from:
  Public GTFS schedules from before and after project opening
  Reported total project ridership
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 22: National Parameter Development
Iterations and model adjustments
  Observations on residuals vs. rider-survey data in previous trials
  Hypotheses on behaviors not yet captured
  Revised relationships, new variables, and/or updated parameters
  New application to full set of systems/projects
  Repeated until plausible explanation of behavior yields an acceptable fit to the data
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 23: National Parameter Development
STOPS calibration and validation based on data that represent a wide range of conditions not found in a single metro area
Solid grasp of:
  Impacts of introducing a new mode that is not currently present in the metro area’s transit system
  Difference between the introduction of a new mode and expansion of an existing fixed-guideway mode
  Sensitivity to changes in service levels – large and small
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 24: National Parameters – Data Sources
Static Calibration
Metro area | Commuter Rail | Heavy Rail | Light Rail | Streetcar | BRT | Local Bus
Atlanta |  | ● |  |  |  | ●
Charlotte |  |  | ● |  |  | ●
Denver |  |  | ● |  |  | ●
Kansas City |  |  |  |  |  | ●
Norfolk |  |  | ● |  |  | ●
Phoenix |  |  | ● |  |  | ●
Salt Lake City | ● |  | ● |  | ● | ●
St. Louis |  |  | ● |  |  | ●
This list, and the list on the next slide, document the metro areas used in the grand recalibration of STOPS for Version 2.5
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 25: National Parameters – Data Sources
Dynamic Validation
Metro area | Commuter Rail | Heavy Rail | Light Rail | Streetcar | BRT
Norfolk |  |  | ● |  | 
Orlando | ● |  |  |  | 
Nashville |  |  |  |  | ●
Denver West |  |  | ● |  | 
Phoenix NW |  |  | ● |  | 
Phoenix Mesa |  |  | ● |  | 
Grand Rapids |  |  |  |  | ●
Seattle |  |  |  | ● | 
NY 2nd Ave. |  | ● |  |  | 
DC Silver Line |  | ● |  |  | 
DC Streetcar |  |  |  | ● | 
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 26: National Calibration Results
Comparison of STOPS vs. Observed Ridership (Dynamic Test)
Chart: Observed Ridership
| 0 | 5012 | 3246 | 14793 | 1289 | 1289 | 14790 | 10192 | 10488 | 3185 | 3185 | 2700 | 147122 | 31450 | 3613 | 5012
Project Ridership | 5594 | 5673 | 11743 | 1464 | 1413 | 14738 | 13906 | 10324 | 3059 | 3156 | 4177 | 138366 | 28210 | 1922 | 7779
Reference | 0 | 5012 | 3246 | 14793 | 1289 | 1289 | 14790 | 10192 | 10488 | 3185 | 3185 | 2700 | 147122 | 31450 | 3613 | 5012
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 27: Two Cautions
1. Details matter
  Effective district and station group definitions
  Accurate count data
  Accounting for special markets
  Simplified ≠ sloppy!!
  (And simplified ≠ sketch, either)
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 28: Two Cautions
2. Forecasting is an uncertain business; some sources of uncertainty:
  The characteristics of the project itself
  Background projections of population and employment
  Differentiation from competing transit systems
  The accuracy of the forecasting tools
Uncertainties must be characterized, quantified, and communicated to decision-makers
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 29: How STOPS Works -- Overview --
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 30: A Typical Transit Forecasting Model
Fundamental structure of:
  Conventional trip-based models
  Newer activity-based models
  STOPS-synthetic
  STOPS synthetic/special markets
  STOPS incremental
In STOPS, mode choice and assignment models come calibrated and validated against national datasets
person trips
transit volumes
TRANSIT TRIPS
highway network
mode choice
assignment
transit network
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 31: Local Calibration of STOPS
Objectives
  Localize the “national” models
    Mode choice
    Transit assignment
  Train the mode choice model to reproduce the transit trips measured in a rider survey
  Invent a set of person-trips that supports the mode choice model in this task
invented person trips
predicted transit volumes
PREDICTED TRANSIT TRIPS
current highway network
localized mode choice
localized assignment
current transit network
Incremental
(Adjusted)
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 32: Local Calibration of STOPS
invented person trips
current transit volumes
CURRENT TRANSIT TRIPS
current highway network
transit survey
current transit counts
CTPP transit%
person trips =
transit trips
÷
transit share
transit trips ≡
survey data trips !!
localized mode choice
localized assignment
current transit network
person-trip builder
person trips =
transit trips
÷
transit share
[adjusted to counts]
Incremental
(Adjusted)
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 33: Local Calibration of STOPS – Honolulu Application
OMPO – 2017 Calibration
  2012 On Board Survey
  2017 APC Data/2015 APC Data
  2015 Population/Employment and highway skim data
Uses transit trips from On-Board Survey to develop person trips
Uses mode share from CTPP
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 34: Forecasting in the Current Year
Application of calibrated STOPS
  Regardless of selected method
    Synthetic
    Synthetic+special markets
    Incremental
  Virtues of current year FIRST
    Clarifies QC checks
    Fosters interpretation
    Helps to identify insights
    (Meets CIG requirements)
predicted person trips
predicted transit volumes
PREDICTEDTRANSIT TRIPS
current highway network
localized mode choice
localized assignment
current transit network
The calibrated model!
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC
Notes: So far all we have done for OMPO is current year – which is actually 2019 count data with 2015 P/E and 2012 OBS. Not ideal but a place to start.

## Slide 35: Forecasting in the Current Year
predicted person trips
No-build transit volumes
NO-BUILD TRANSIT TRIPS
current highway network
localized mode choice
localized assignment
No-build transit network
predicted person trips
Build transit volumes
BUILD TRANSIT TRIPS
current highway network
localized mode choice
localized assignment
Build transit network
=changed from the validation forecast
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 36: Forecasting in a Horizon Year
future person trips
No-build transit volumes
NO-BUILD TRANSIT TRIPS
future highway network
localized mode choice
localized assignment
No-build transit network
future person trips
Build transit volumes
BUILD TRANSIT TRIPS
future highway network
localized mode choice
localized assignment
Build transit network
= changed from the validation forecast
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC
Notes: Not yet accomplished for OMPO Application: Need future network and demographic data/person trip data

## Slide 37: Quick Note on Highway Components
No highway network, path-building, or speed estimation
  Imported AM peak LOV zone-to-zone times, distances
  Current year and, if needed, future year(s)
  Same zone system as for population and employment
  Source: regional travel model
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC
Notes: NOTE – This is where it would be helpful to have 2019 pop/emp/zone to zone times/distances if available. Current year 2019 is using 2017 information (or 2015 information)

## Slide 38: OMPO STOPS Topics
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC
Inputs – Networks and Other Data
Schedule-Based Transit Path-Builder
Current Year Travel Patterns
Initial Travel Patterns for STOPS-Incremental

## Slide 39: Inputs – Networks and Other Data
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 40: Input Data
GTFS based transit network
  Best representation of current year data
  Strategy for incorporating build network changes is important (avoid inadvertent errors)
On Board Survey data (OMPO 2012)
  used to establish trip patterns and inform person trips
APC data for calibration year (2017)
  Used to provide more robust local detail and inform person trips
APC data for calibration year (2019)
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 41: GTFS
Obtained from TheBUS (calibration and validation) and DTS (build)
Captures all the detailed info in the public schedule
  Routes.txt
  Calendar.txt
  Trips.txt
  Stops.txt
  Stop_times.txt
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 42: Route types GTFS vs STOPS
Each route is designated as one route type over its entire length
Code | GTFS definition | STOPS definition
0 | Tram,streetcar or light rail | Partial fixed guideway
1 | Subway or metro | Full fixed guideway
2 | Intercity rail | Full fixed guideway
3 | Bus | Bus
4 | Ferry | Full fixed guideway
5 | Cable car | Full fixed guideway
6 | Gondola/suspended cable car | Full fixed guideway
7 | Funicular | Full fixed guideway
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 43: Honolulu STOPS – GTFS updates
Implications for route_type Coding
  Rail changed to route type 1
  Bus remains route type 3
Supplemental information
  Rail stations – flagged as project stations in stops.txt file; station type adjusted for grade separation
  Station groups – defined based on districts for validation/calibration; create rail group for project;
  PNR lots – defined in a separate file if needed
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC
Notes: *No PNR lots defined in 2019 build run to date;

## Slide 44: Access/Egress Connections
Access, egress – utilized OMPO shape file of walkable streets. For each zone centroid and each eligible transit stop:
WALK: distance along streets at 3 mph within 1.4 miles;
KnR: airline distance at speed computed from MPO zone-to-zone time to any stop within 3 miles of a PnR lot; and
PnR: airline distance at computed KnR speed to user designated PnR lots within catchment distance specified for the lot (depending on nature of the lot can be 3, 6, 10 or 25 miles)
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 45: Transfer Connections
Transfers (by STOPS):
For two kinds of ‘transfers’
  Transit stop to transit stop
  PnR lot to transit stop
For any transfer up to 0.25 airline miles
Always based on airline miles, even with presence of walk network for access
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 46: Schedule-Based Transit Path-Builder
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 47: Transit Paths and Impedances
Two time periods:
AM Peak
  8-9 AM
  one of six possible arrival times
Midday
  1-2 PM
  One of six possible arrival times
Three access types
  Walk, kiss-n-ride, park-n-ride
Three path types
  FG only, Bus only, FG-Bus
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC
Notes: Path builder finds the best path of each combination;
Mode-choice model predicts trip shares that will use the paths
*remember peak period problem with routes serving military bases – FTA to investigate change of time

## Slide 48: Schedule-Based Path Selection
Generalized cost to identify best path*:
  In-vehicle time (weight=1.0 minute per minute)
  Walk time (weight=1.5 minutes per minute)
  PnR and KnR time (weight=1.5 minutes per minute)
  Wait time (weight=1.0 minutes per minute)
  Boarding penalty (5 minutes per boarding)
  Reduced by 5 minutes if both FG and Bus are in path (to find FG-Bus paths that are competitive but not the lowest impedance)
  * Generalized cost expressed in weighted minutes
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC
Notes: More detail on pgs 41 and 42 of course notebook –

## Slide 49: Current Year Travel Patterns
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 50: Important Note:
Person trips in STOPS will not match MPO estimates and should not be used outside STOPS
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 51: Definitions
Trip tables – trips in a metro area aggregated to the zone to zone (Z2Z) level, often stratified by their purposes, modes and traveler characteristics
  Person trip tables = travel by all modes
  Transit trip tables – travel on transit
District to district (D2D) tables – zone-to-zone tables aggregated to larger subareas for easier analysis and review of results
Travel patterns – distillation of key travel markets, characterized by their flows from O to D, purposes, modes and traveler characteristics
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 52: Initial Travel Patterns for STOPS-Incremental
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 53: OMPO Calibration of STOPS
invented person trips
current transit volumes
CURRENT TRANSIT TRIPS
current highway network
transit survey
current transit counts
CTPP transit%
transit trips ≡
survey data trips !!
localized mode choice
localized assignment
current transit network
person-trip builder
person trips =
transit trips
÷
transit share
[adjusted to counts]
Incremental
(Adjusted)
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 54: For STOPS Incremental (Honolulu)
Need transit trips (2012 OBS) and person trips (in a supporting role)
Reverse of calculations in a traditional 4-step model
Uses survey data to establish transit trips
Person trips are a multiple of transit trips (they are developed by STOPS not input directly from MPO model)
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 55: Why do it this way?
Resulting current year transit trip table is directly from survey data
  Better understanding of reality than a model produced estimate
  STOPS modeled transit trips match the survey data in:
    Aggregate number of trips
    District-to-District flows
    Zone specific location of transit trip-ends reported in survey
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC
Notes: Captures some of the unique travel patterns on Oahu – but OBS understands it.

## Slide 56: Mode and Path Choice
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 57: Overview
Path builder for each i-j zone pair:
  Finds best path for each combination of access and path-type
  Looks for paths separately for HBW/peak and Non-Work/off-peak
Mode/access/path choice model for each i-j:
  Evaluates each potential path on its attractiveness using path parameters
  Computes shares based on the relative “scores”
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 58: STOPS Mode Choice
Discrete choices
  Transit, non-transit
  Transit(best paths i-j):
    Access mode:
    walk,
    KNR,
    PNR
    Path type:
    FG only,
    Bus only,
    Bus and FG
Market Segments
  Trip purposes:
    HBW, HBO, NHB
  Car ownership:
    0car, 1car, 2+car
  Times of day:
    Peak (HBW)
    Mid-day (HBO, NHB)
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 59: Mode and Access Choice in STOPS
All-mode person trips from i to j
Non-Transit
Auto
Walk
Transit
Walk
KnR
PnR
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 60: Path Choice in STOPS
Access Mode
FGO
FGB
BusO
KEY:
FGO=Fixed Guideway Only
BusO=Bus Only
FGB=Fixed Guideway+Bus
Fixed Guideway Setting (FGS) at full value when FG path includes any of route types 1, 2, 4-7
Partial FGS applies when FG path involves route type 0 only
Smaller FGS values: sharper competition (winner takes all)
Larger FGS values: gentler competition (losers get significant shares)
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC
Notes: Non included attributes shown with FGSetting values

## Slide 61: Mode/Access/Path Choice: Guideways
Objectives – to represent appropriately:
  ‘other’ attributes of each FG
  Competition among available path choices
Tools available to users:
  Route_type classification
  (for OMPO STOPS: FG=1, Bus=3)
  Fixed guideway settings
Approaches (consult with FTA)
  All bus system with new FG – assertion (FGS=1) and testing (more to come)
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC
Notes: Honolulu Rail is a clearly defined rail corridor so the full FGSetting is 1.0. Other future options should consult STOPS documentation and FTA Help Desk; for example a streetcar might have a FGS of less than 1.0; important to be cautious in the future as there are only three path type options available so as the system grows or changes from bus/fixed guideway these parameters will likely change for new things.

## Slide 62: Calibrations and Test Run
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC
2017 Calibration
2019 Calibration
2019 Rail Test
OMPO Next Steps

## Slide 63: 2015 & 2017 Calibration

## Slide 64: 2015 and 2017 Calibration
FTA developed for use in STOPS Training
Updated with 2017 APC data
Provided as base for OMPO STOPS Application
  2012 OBS
  2015 Pop/Emp
  2017 APC
  OMPO Zones (764)
  26 Districts
  26 Station (Stop) Groups
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 65: Honolulu STOPS - Groupings
Station Groups
  Aggregations of stations/stops
    To refine understanding of transit travel patterns STOPS obtains from OBS and CTPP
    Enable introduction of generally reliable data on geographic locations of transit activity
  Station Group good practice
    Up to a max of 250 available (26 in OMPO STOPS)
    Initially align with districts – OMPO STOPS
    Can fine tune by creating Project Station Group (Station Group 27 added for RAIL in BLD)
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 66: Honolulu STOPS - Groupings
Stop Groups/Districts
  From 2017 Calibration (26)
  Used for reporting and analysis
  Sized to encompass homogeneous areas but large enough to reduce data noise and support calibration outcomes
  Good strategy to follow includes:
    CBD
    Other major activity centers
    Finer districts near project areas
    Coarser aggregations outside large transit markets
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 67: Honolulu District Structure (26)
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 68: Honolulu District – Project Area
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 69: Honolulu Districts
Number | Name
1 | CBD
2 | Kakaako
3 | MAKIKI
4 | WAIKIKI
5 | KAIMUKI/WAILALAE
6 | KALIHI/NUUANU
7 | IWILEI
8 | AIEPORT/PH
9 | SALTLAK/HALAWA
10 | PEARL CITY
11 | EWA
12 | KAPOLEI
13 | MAKAKILO
Number | Name
14 | WAIPAHU
15 | WAIAWA
16 | MILILANI
17 | WAHIAWA/SCHOF
18 | E HONOLULU
19 | KANEOHE
20 | KAILUA
21 | WINDWARD
22 | NORTH SHORE
23 | WAIANAE
24 | MANOA
25 | UHMANOA
26 | ALAMOANA
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 70
Route_ID | Route Name | 2017 APC Count | 2017 STOPS
2 | 2-Waikiki-School-Middle | 14720 | 16018
127 | 13-Liliha-Waikiki-University | 13012 | 6301
22 | A-City Express! A | 12957 | 15475
1 | 1-Kaimuki-Kalihi | 12127 | 8925
3 | 3-Kaimuki-Salt Lake | 11159 | 10197
26 | 40-Honolulu-Makaha | 9580 | 6149
28 | 42-Ewa Beach-Waikiki | 9362 | 7327
4 | 4-Nuuanu-Punahou | 6421 | 5895
40 | C-Country Express! C | 5885 | 7523
109 | E-Country Express! E | 5588 | 12631
131 | 62-Honolulu-Wahiawa | 5527 | 5927
126 | 9-Kaimuki-Pearl Harbor | 5379 | 4262
6 | 6-Pauoa-Woodlawn | 5264 | 4073
18 | 19-Waikiki-Airport-Hickam | 4423 | 3976
102 | 1L-School Street-Hawaii Kai | 4267 | 8526
Notes: 2017 Calibration – top 15 routes (source results.prn table 10.01)

## Slide 71: Observations on 2017 Calibration
Use of 26 stop groups (same as 26 districts)
  More details definition of stop groups
  Individual Route calibration
Path Choice Complexities
  Express routes

## Slide 72: 2019 Calibration
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 73: Honolulu – 2019 Current Year
Updated APC to 2019 data
Updated GTFS to 2019 bus
Could not update 2015 demographics or highway LOS
2017 Calibration control file revised to point to 2019 inputs
Zones, Districts, Station Groups remain the same
Current Year = NoBuild for Honolulu 2019
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 74
Route_ID | Route Name | 2019 APC Count | 2019 Base STOPS
2 | 2-Waikiki-School-Middle | 17680 | 12363
1 | 1-Kaimuki-Kalihi | 13238 | 8515
127 | 13-Liliha-Waikiki-University | 11995 | 6934
22 | A-City Express! A | 11433 | 14397
3 | 3-Kaimuki-Salt Lake | 9403 | 8750
28 | 42-Ewa Beach-Waikiki | 8228 | 6859
26 | 40-Honolulu-Makaha | 8147 | 4937
4 | 4-Nuuanu-Punahou | 5521 | 5026
109 | E-Country Express! E | 4838 | 12187
126 | 9-Kaimuki-Pearl Harbor | 4800 | 3309
40 | C-Country Express! C | 4672 | 6692
6 | 6-Pauoa-Woodlawn | 4547 | 3699
131 | 51-Honolulu-Wahiawa | 4545 | 4755
18 | 19-Waikiki-Airport-Hickam | 4229 | 3967
139 | 60-Honolulu-Kaneohe-Haleiwa | 3590 | 5455
Notes: 2019 Calibration – Comparison of top 15 routes (source: results.prn table 10.01)

## Slide 75: 2019 Rail Test Run

## Slide 76: Recommended Next Steps
Contact FTA Help Desk to resolve peak period issue for zero rider routes
Could refine station groups to break up into smaller route groups (max of 250 available)
Review rail test run GTFS networks for consistency with 2019 calibration GTFS
Could add PNR lots for rail test run (consult with FTA Help Desk)
Could consider visitors as an external add in to STOPS (consult with FTA Help Desk)
ATTEND NTI/FTA STOPS TRAINING

## Slide 77: STOPS File Structure
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 78: Housekeeping Details:
Each STOPS run prepares three forecasts in parallel:
  Current Year
  Nobuild
  Build
For the initial 2019 Calibration all three are set to the 2019 Bus system without the rail line
The parameter file is based on the 2017 Calibration with the input GTFS updated to point to 2019 files.
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 79: STOPS File Structure
Honolulu_2019
Districts
GTFOutput
Inputs*
Logfiles
OutputData
Reports
Scratch
Skims
Stops
Honolulu_2019.ctl*
OP_TR_BLD-
OP_TR_EXST
OP_TR_NOBL
PK_TR_BLD
PK_TR_EXST
PK_TR_NOBL
DEC19
*Required files for to start a run, others are created by STOPS
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 80: Notes to Remember
Some inputs are not scenario specific and should always be carried forward as INPUTS:
District definition file
Forecast-year definition file
Station file (and stop_IDs)
Walk-links shape files
MPO information (including TAZ system)
CTPP files (including CTPP zone system)
  Note: STOPS geographically overlays MPO and CTPP zones
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 81: The STOPS Interface-How to Run It!
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 82: The STOPS Graphical User Interface
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 83: STOPS Getting Started
Create new run folder
Copy INPUTS and .ctl from previous run
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 84: STOPS File Structure
Paste INPUTS and .CTL from previous STOPS run
STOPS will generate all remaining folders for a model run but these two are essential to start.
There are several key items that should always be in the INPUTS folder.....
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 85: INPUTS Folder – OMPO 2019 BLD
GTFS Files for Existing NoBuild and Build
ACS/CTPP, MPO demographic and highway files, walk links, district/TAZ equivalencies and data from calibration.
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC
Notes: For a particular set of STOPS runs, it is common practice to copy the inputs file from run to run while adding new GTFS as needed. This ensures that the data used to develop the STOPS Calibration and the proceeding model runs stays together. This is a place where FTA Help Desk consultation could be helpful.

## Slide 86: STEPS to Configure STOPS
Step 1. Create/select parameter file
Step 2. Edit parameter file
Step 3. List and check TAZ & CTPP filenames
Step 4. Define forecast years
Step 5. List and check GTFS files
Step 6. Specify station locations
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 87: Step 1. Select/Edit Parameter File
Select .ctl file
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 88: Step 1. Select/Edit Parameter File
honolulu2019.ctl file exists – based on previous Calibration parameters
Possible edits include GTFS updates/Model Run Name identifier
STOPS has the ability to create a parameter file from scratch. But there’s no need for that with OMPO STOPS application as it’s been done!
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 89: Purpose of the Parameter File
✅ Defines the geography type of the CTPP (ACS) data
✅ Identifies the appropriate state and MPO
⁉️ Identifies subfolder location of each GTFS file set
✅ Provides trip rates by purpose and autos owned
✅ Provides linked transit trips by purpose and autos owned
⁉️ Specifies the fixed guideway settings
✅ Specifies the CTPP-transit calibration method
✅ Specifies the station-group calibration method
⁉️ Sets the transfer penalty and access mode parameters
Where, ✅ indicates items already set for Honolulu and,
⁉️ indicates items that may change for BLD runs
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC
Notes: This file is the ‘nerve center’ of a STOPS application – all the important parameters and inputs are specified here.

## Slide 90: honolulu2019.ctl
Possible Updates:
Run Name
GTFS Files
Schedule Day
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC
Group Calibration = 10 does not change
Notes: Group Calibration = 10 always stays the same for OMPO Application as OBS was available initially.

## Slide 91: Steps to Configure STOPS
Step 1. Create/select parameter file
Step 2. Edit parameter file
Step 3. List and check TAZ & CTPP filenames
Step 4. Define forecast years
Step 5. List and check GTFS files
Step 6. Specify station locations
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 92: Step 3. List and check TAZ/CTPP files
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 93: Step 4. Define forecast years
Define Forecast Years
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 94: Step 4. Define forecast years
Define Forecast Years❓
CTPP –do not change
2015Pop/Emp – could be changed?
Weekday Unlinked Transit Trips – from 2012 OBS – do not change!
❓
❓
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 95: Step 5. List and check GTFS files
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 96: Step 6. Specify station locations
Specify Station Locations
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 97: Step 6. Specify station locations
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 98: Step 6. Specify station locations
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 99: Steps to prepare data...
Step 7. Create station buffers (reads station file and selects zones within 25 miles)
Step 8. Define districts, station groups and zonal data (already specified for OMPO)
Step 9. Create MPO-TAZ equivalency (reads CTPP and MPO TAZ layers; create equivalency; assign MPO demographics to CTPP zones)
Step 10. Prepare pedestrian environment (determine census blocks per square mile for each zone)
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC
Notes: These steps don’t require any interaction – just need to be run.

## Slide 100: Steps to RUN STOPS
Step 11. Run Batch Steps
  CTPP Extract (read CTPP, create trip/skim shell for each scenario)
  GTF Path (build transit paths/skims)
  GTF Post (post transit skims to trip/skim file)
  Prepare Forecast Years (grow trips in trip/skim file for horizon year)
  STOPS (run demand model to predict ridership for current, no-build, build)
Step 12. Report STOPS Results (report file tables)
Step 13. Map STOPS Results (open GIS to view thematic maps)
Step 14. Z2Z Query (show skims/trips for a particular interchange)
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 101: Results of a STOPS Run
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 102: Results Table Directory
Automatically saved in ‘results’ subdirectory
Filename ends with results.prn
Opens in notepad or text editor window
Contains 15 sections
Easiest to find the table by searching on the table number
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 103
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC
Notes: Report File Index, part 1

## Slide 104
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC
Notes: Report file and index, part 2

## Slide 105
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC
Notes: Report file and index, part 3 – section 15 see next slide for description

## Slide 106: Report File Index Table 15
Lists table numbers in the Table 15 matrix
Every table is also a matrix – D2D or Station to Station in P/A format
Columns represent the type of trip reported
Rows represent the statistic, trip purpose and auto ownership levels included in each table
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 107: Table 15 Column Definitions
  Transit Trips
    Transit Path Type
      FGO – Fixed guideway only
      FGB – Fixed guideway and bus
      BUS – Bus only
      TRN – Any transit (sum of above)
      FG – Any fixed guideway (sum of FGO and FGB)
    Access Mode
      WLK – Walk
      KNR – Kiss and Ride
      PNR – Park and Ride
      All – Sum of the above access modes
  Total Person Trips
    All Mode – the estimate of person trips used to generate the estimate of transit trips
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 108: Table 15 Row Definitions
Statistic
  Scenario
    Existing
    No-build
    Build
  Matrix Type
    District to district linked trips
    Station to station total flows
  Other
    Incremental (Build – No-Build) district to district linked trips
    Linked Trips on project – D2D linked trips that use the project
    Station to station project flows – statistic usage by project flows
Trip Purpose
  HBW – Home based work
  HBO – Home based other
  NHB – Non home based
  ALL – sum of above
Household Auto Ownership
  0 – 0 cars in household
  1 - 1 car in household
  2 – 2 or more cars in household
  ALL – sum of above
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 109: Accessing Results
R-Script to support working with output
Set up to extract select tables from results.prn
Generates each as a separate CSV and TXT file
Options for selecting desired tables depending on STOPS run needs
Developed and supported by WSP
OMPO STOPS Training WSP/Dunbar Transportation Consulting LLC

## Slide 110: R-Script

## Slide 111: Tables might vary with application but here are a few suggestions:
  2.05 – station group boarding factors – check for reasonableness
  4.01/2/3/4-Linked Weekday Transit Trips all purposes (Build, Incremental and Project)
  5.01/2/3/4 – Linked Weekday Transit Trips on FG
  9.01 – Station Boardings by Mode of Access (Existing, NoBuild and Build)
  10.01 – Route boardings by mode of access
  11.01/2/3/4- Summary of trips by purpose, submode, access mode, auto ownership and scenario